## Slide 1: The Power of Programmable Parsing
P4: Programming Protocol-Independent Packet Processors
ACM CCR. Volume 44, Issue #3 (July 2014)
Dan Talayco
Barefoot Networks
November 2014

## Slide 2: Protocols
Protocols are what allow networking to work
There are a lot of protocols out there already
TCP
UDP
IPv4
IPv6
DCTCP
SNAP
Ethernet
RIP
OSPF
HTTP
SSL
ARP
RARP
BGP
FLIP
GRE
NVGRE
GENV
CAPWAP
IBGP
VLAN
PPP
L2TP
ICMP
POP
FTP
SMTP
POP
IMAP
IP
MPLS
BFD
FCOE
SCTP
ERSPAN
IPSEC
NSH
Notes: Assuming familiarity with OF model, match+action as the right way to model the fundamental operation of the data plane. Will discuss P4 which takes on the pesky questions of complete specification of action semantics and of control flow. But for today, looking at low hanging fruit of…. The parser.

## Slide 3: Protocols Evolve
Protocols change
  New encapsulations: VXLan, NVGRE, GENV…
Notes: Protocols are agreements between two agents on the meaning of information.
Layers are important, but not pure
  Pseudo header for TCP/UDP checksums
This coupling complicates parsing

## Slide 4: Protocols Evolve
Protocols change
  New encapsulations: VXLan, NVGRE, GENV…
And we want them to be extensible
  For example, option lists in headers
    Variable length lists
    Variable length options
    New type values over time
Notes: Protocols are agreements between two agents on the meaning of information.
Layers are important, but not pure
  Pseudo header for TCP/UDP checksums
This coupling complicates parsing

## Slide 5: Networks are Diverse
Seeing the growth of MSDCs and other networks with high performance demands
  Requirements fundamentally different from e.g. WAN
Network performance has become a competitive advantage
Deployments are becoming more specialized.
  Yes, we can adapt BGP to work to the TOR or even the v-Switch, but is there a better way?
“One size fits all” is no longer acceptable

## Slide 6: Networks are Diverse
Seeing the growth of MSDCs and other networks with high performance demands
  Requirements fundamentally different from e.g. WAN
Network performance has become a competitive advantage
Deployments are becoming more specialized.
  Yes, we can adapt BGP to work to the TOR or even the v-Switch, but is there a better way?
“One size fits all” is no longer acceptable

## Slide 7: Networks are Diverse
Seeing the growth of MSDCs and other networks with high performance demands
  Requirements fundamentally different from e.g. WAN
Network performance has become a competitive advantage
Deployments are becoming more specialized.
  Yes, we can adapt BGP to work to the TOR or even the v-Switch, but is there a better way?
“One size fits all” is no longer acceptable

## Slide 8: Parsing
Protocols are defined by field semantics
…and parsers identify fields
Yet parsers have not gotten much attention
  Too easy? Just a state machine
  Too hard? Difficult to make programmable and line rate
  Too important? Controlling the protocols means controlling the feature set

## Slide 9: Parsers are Stuck in the Past
Static Parsing Slows Innovation
  Binds feature changes to slower development cycle (esp in HW, but SW too).
OpenFlow History
  Avoided taking on the challenge; just identified fields for match/action
  Field count, 1.0 to 1.4: 12 => 15 => 36 => 40 => 41

## Slide 10: Programmable Parsers
Programmable parsing is the key to unlocking OpenFlow’s Match+Action processing model
Obviously, possible in SW
  But not (yet) in OVS
Also possible in HW
  Gibb, et al, Design Principles for Packet Parsers

## Slide 11: High Level Language Support
The P4 language
  Based on an abstract forwarding model
  With a programmable parser
  Allows the definition of arbitrary headers and fields
  Provides a context for match+action definitions

## Slide 12
I
N
P
U
T
O
U
T
P
U
T
P
A
R
S
E
R
Match
Action
Queues
and/or
Buffers
Switch Configuration
Match+Action Table Config
Parse
Graph
Run Time Forwarding rules
Match
Action
Control
Program
Ingress Match+Action
Egress Match+Action
Packet Modifications +
Egress Selection
Packet Modifications
High Level P4 Abstraction

## Slide 13: Headers and Fields
header_type ethernet_t {
fields {
dstAddr : 48;
srcAddr : 48;
etherType : 16;
}
}
/* Instance of eth header */
header ethernet_t inner_ethernet;
header_type egress_metadata_t {
fields {
nhop_type : 8; /* 0: L2, 1: L3, 2: tunnel */
encap_type : 8; /* L2 Untagged; L2ST; L2DT */
vnid : 24; /* gnve/vxlan vnid/gre key */
tun_type : 8; /* vxlan; gre; nvgre; gnve*/
tun_idx : 8; /* tunnel index */
}
}
metadata egress_metadata_t egress_metadata;
Metadata is a header instance
Fields have a width and other attributes
Headers are collections of fields
These are types which are used to declare instances
Notes: From glass/parser/examples/dc_genv_lat + additions
Note time stamps
Discuss metadata (field granularity) vs packet headers; tag stacks; field attributes like signed, saturating, etc.
----- Meeting Notes (6/24/14 16:48) -----
Syntax highlighting!
Fix declaration syntax for header instances.
Discuss type/instance; visually combine

## Slide 14: Headers and Fields
header_type ethernet_t {
fields {
dstAddr : 48;
srcAddr : 48;
etherType : 16;
}
}
/* Instance of eth header */
header ethernet_t inner_ethernet;
header_type egress_metadata_t {
fields {
nhop_type : 8; /* 0: L2, 1: L3, 2: tunnel */
encap_type : 8; /* L2 Untagged; L2ST; L2DT */
vnid : 24; /* gnve/vxlan vnid/gre key */
tun_type : 8; /* vxlan; gre; nvgre; gnve*/
tun_idx : 8; /* tunnel index */
}
}
metadata egress_metadata_t egress_metadata;
Type used in Instance Declaration
Fields have a width and other attributes
Headers are collections of fields
These are types which are used to declare instances
Notes: From glass/parser/examples/dc_genv_lat + additions
Note time stamps
Discuss metadata (field granularity) vs packet headers; tag stacks; field attributes like signed, saturating, etc.
----- Meeting Notes (6/24/14 16:48) -----
Syntax highlighting!
Fix declaration syntax for header instances.
Discuss type/instance; visually combine

## Slide 15: The Parser
parser parse_ethernet {
extract(ethernet);
return select(latest.etherType) {
ETHERTYPE_CPU : parse_cpu_header;
ETHERTYPE_VLAN : parse_vlan;
ETHERTYPE_MPLS : parse_mpls;
ETHERTYPE_IPV4 : parse_ipv4;
ETHERTYPE_IPV6 : parse_ipv6;
ETHERTYPE_ARP : parse_arp_rarp;
ETHERTYPE_RARP : parse_arp_rarp;
ETHERTYPE_NSH : parse_nsh;
}
}
Imperative functions for “states”
Extract header instances
Select a next “state” by returning a parser function
Produces a Parsed Representation of the packet
Notes: “nsh” is network service header, ietf quinn.
CPU header is from dc_genv.
#defines C pre-processor; use of current. Extracting to tag stacks.

## Slide 16: The Parser
parser parse_ethernet {
extract(ethernet);
return select(latest.etherType) {
ETHERTYPE_CPU : parse_cpu_header;
ETHERTYPE_VLAN : parse_vlan;
ETHERTYPE_MPLS : parse_mpls;
ETHERTYPE_IPV4 : parse_ipv4;
ETHERTYPE_IPV6 : parse_ipv6;
ETHERTYPE_ARP : parse_arp_rarp;
ETHERTYPE_RARP : parse_arp_rarp;
ETHERTYPE_NSH : parse_nsh;
}
}
Imperative functions for “states”
Extract header instances
Select a next “state” by returning a parser function
Produces a Parsed Representation of the packet
Notes: “nsh” is network service header, ietf quinn.
CPU header is from dc_genv.
#defines C pre-processor; use of current. Extracting to tag stacks.

## Slide 17: The Parser
parser parse_ethernet {
extract(ethernet);
return select(latest.etherType) {
ETHERTYPE_CPU : parse_cpu_header;
ETHERTYPE_VLAN : parse_vlan;
ETHERTYPE_MPLS : parse_mpls;
ETHERTYPE_IPV4 : parse_ipv4;
ETHERTYPE_IPV6 : parse_ipv6;
ETHERTYPE_ARP : parse_arp_rarp;
ETHERTYPE_RARP : parse_arp_rarp;
ETHERTYPE_NSH : parse_nsh;
}
}
Imperative functions for “states”
Extract header instances
Select a next “state” by returning a parser function
Produces a Parsed Representation of the packet
Notes: “nsh” is network service header, ietf quinn.
CPU header is from dc_genv.
#defines C pre-processor; use of current. Extracting to tag stacks.

## Slide 18: Parsing and Headers Give Context for Match + Action
table acl {
reads {
ipv4.dstAddr : ternary;
ipv4.srcAddr : ternary;
ipv4.protocol : ternary;
udp.srcPort : ternary;
udp.dstPort : ternary;
ethernet.dstAddr : exact;
ethernet.srcAddr : exact;
ethernet.etherType : ternary;
}
actions {
no_op; /* permit */
acl_drop; /* reject */
nhop_set; /* policy-based routing */
}
}

## Slide 19: Programmable Parsing in OVS
Supporting a programmable parser in OVS is tractable
OVS is critical for providing deployment specific features in the future
  Selective protocol engagement
  Agile response to protocol evolution
  Overlay/underlay architectures

## Slide 20: The P4 Language Consortium
Consortium: Independent, open-source, CA non-profit.
Original authors from Google, Microsoft, Intel, Princeton, Stanford, Barefoot
Sign up for the P4 Announcement mailing list: www.p4.org
  Currently on the site: P4 Language Spec, the original paper, reference links