## Slide 1: Ingress Scheduling in OvS-DPDK
Billy O’Mahony – Intel Jan Scheurich – Ericsson
November 16-17, 2017 | San Jose, CA
Notes: My name is Jan Scheurich, I’m working with Ericsson in the Cloud S&T organization.
I’m responsible for data plane characteristics in our NFVI solution.
As part of that I’m heading the Ericsson team working upstream with OvS.

## Slide 2: Introduction
Use cases for traffic prioritization in NFV
State of the art in OvS-DPDK datapath
Rx queue prioritization in DPDK datapath
Traffic classification and queue selection on NIC
Next steps
Notes: I will start with giving you the background why Quality of Service in general and traffic prioritization in particular is a crucial feature in OvS for robust and performing Network Function Virtualization deployments.
We will then have a look at how OvS-DPDK today is equipped in this respect and provide measurement results demonstrating that today it is not able to provide the required protection of critical traffic.
Next Billy will present his ongoing RFC work to enhance OVS-DPDK with ingress scheduling capabilities. That comprises two parts: the concept of Rx queue priorities and the off-load of queue selection to the NIC HW. We’ll have a look at first test results to check the effectiveness of the approach.
We will end with an outlook on the planned and needed work to upstream the current RFC patches.

## Slide 3: Scenario: NFVI on Converged Data Center VIM control plane sharing physical network with tenant data
Compute Node
OvS
ToR A
ToR B
dpdk0
dpdk1
br-int
br-ctl
Tenant VM
Tenant VM
VXLAN or Geneve tunnels
vhostuser
Local Agents
Local Agents
Local Agents
VIM Components
Host networking
bond
br-prv
tag
tag
VIM = Virtual Infrastructure Manager For example OpenStack component: Nova, Neutron services and their local agents
Notes: In Network Function Virtualization Telco operators virtualize their typical control and data plane nodes on a cloud infrastructure, with all the implications on characteristics like performance and availability.
One of the characteristics of co-called Converged Data Center HW is that a common shared network fabric carries all classes of traffic: tenant data, storage, but also Virtual Infrastructure Manager control plane. We cannot always assume the existence of dedicated out-of-band networks.
This requires proper traffic separation and QoS, not only on the fabric but also on the compute hosts themselves, to guarantee that excessive tenant data or storage traffic cannot starve the infrastructure control plane and disrupt its service.
In the example case shown here, the VIM components executing on the compute host OS use the host networking stack and get network connectivity through the LOCAL bridge port of the bridge br-ctl. br-ctl is connected through tagged patch ports to the provider bridge br-prv containing the bond on the physical network fabric.
The tenant data switched in br-int is transferred on the same network fabric either VLAN tagged or through a mesh of overlay tunnels, typically VXLAN or Geneve.

## Slide 4: Use Case 1: In-band OvS Control Plane
Compute Node
OvS
ToR A
ToR B
dpdk0
dpdk1
br-int
br-ctl
Tenant VM
Tenant VM
vhostuser
Local Agents
Local Agents
Local Agents
VIM Components
Host networking
bond
br-prv
tag
tag
LACP bond supervision
VXLAN or Geneve tunnels
LACP = Link Aggregation Control Protocol Here: in-band heart-beat between OVS and each ToR
Notes: The first mandatory use case for traffic prioritization are in-band control protocols terminated by OVS itself, which necessarily share the physical network with tenant data.
The first example is the Link Aggregation Control Protocol, which OVS runs toward the pair of ToR switches to supervise the links of the bond.

## Slide 5: Use Case 1: In-band OvS Control Plane
Compute Node
OvS
ToR A
ToR B
dpdk0
dpdk1
br-int
br-ctl
Tenant VM
Tenant VM
vhostuser
Local Agents
Local Agents
Local Agents
VIM Components
Host networking
bond
br-prv
tag
tag
BFD tunnel monitoring
BFD packets are sent inside tunnel
VXLAN or Geneve tunnels
BFD = Bidirectional Forwarding Detection Here: Heart-beat between OVS instances connected through tunnel mesh
Notes: The second example is the Bidirectional Forwarding Detection protocol, which OVS in our case runs directly through the mesh of overlay tunnels to monitor the connectivity between each pair of compute nodes on the data center.
In this case the BFD packets are encapsulated in VXLAN or Geneve tunnel headers when transported on the physical fabric.

## Slide 6: Use Case 2: VIM Control Plane
Compute Node
OvS
ToR A
ToR B
dpdk0
dpdk1
br-int
br-ctl
Tenant VM
Tenant VM
vhostuser
Local Agents
Local Agents
Local Agents
Nova, Neutron, …
Host networking
bond
br-prv
tag
tag
VIM Control Plane
VXLAN or Geneve tunnels
VIM Control Plane In OpenStack: RabbitMQ, REST APIs calls, …
Notes: The second use case comprises all control plane protocols inside the domain of the Virtual Infrastructure Manager.
If we are considering OpenStack with and SDN networking solution this would for example comprise the HTTP REST APIs, database traffic and the Rabbit MQ message bus between, for example, Nova and Neutron services and their local agents on the compute nodes.

## Slide 7: Use Case 2: VIM Control Plane
Compute Node
OvS
ToR A
ToR B
dpdk0
dpdk1
br-int
br-ctl
Tenant VM
Tenant VM
vhostuser
Local Agents
Local Agents
Local Agents
VIM Components
Host networking
bond
br-prv
tag
tag
OvS control plane: OpenFlow and OVSDB
VXLAN or Geneve tunnels
OpenFlow and OVSDB are special cases of VIM control plane
Notes: I would like to high-light a special case here explicitly:
Also the OpenFlow and OVS control plane between an SDN controller and the OVS instances on all compute nodes is part of the VIM control plane that needs protection against tenant data overload.

## Slide 8: Status Quo in OvS DPDK Datapath
OvS
NIC
PMD 1
PMD 2
ovs-vswitchd thread
Tenant VM
BFD
LACP
RSS
HW Scheduler
VIM Components
Host networking
br-ctl
Notes: Let’s now have quick look of the OVS DPDK datapath today forwards packets.
The Rx queues both of physical NICs as well as tenant vhostuser ports are polled round-robin by a family of PMD threads that process polled packets in run-to-completion.
Processed packets are inserted into Tx queues, as in the case of OVS in-band control plane like BFD and LACP subject to update protocol state machines. Physical NICS typically feature a dedicated Tx queue per PMD to allow lockless operation.
Ports on the host OS, such as the br-ctl bridge port, are instead polled by the main ovs-vswitchd thread. That thread also acts on behalf of the LACP and BFD state machines and transmits packets periodically or in response to state transitions.
It is important to note the asymmetry here: While the ovs-vswitchd thread has its own Tx queue in the NIC, the control plane traffic received from the fabric shares the Rx queues with the tenant data traffic .

## Slide 9: Scenario: PMD Overload
OvS
NIC
PMD 1
PMD 2
ovs-vswitchd thread
Tenant VM
br-ctl
BFD
LACP
RSS
PMD cycles exhausted through tenant data
Rx queues full. Data and control packets dropped.
VIM Components
Host networking
Notes: In the first overload scenario the PMDs are overloaded by excessive tenant data packets (green) arriving on the physical port and destined to the VM.
[This is can very well happen with small packets and applications that do not have an effective congestion avoidance mechanism. An artificial but frequent case are synthetic load generators for benchmarks .]
The PMDs cannot cope with the load so that the NIC’s Rx queues run full and the NIC starts shedding excess packets. Control plane packets (orange) intermixed with tenant data have the same likelihood of being dropped as tenant data packets, even though they may only constitute a very small fraction of the total traffic.
Up to a certain loss level control plane transport protocols may compensate and endure but sooner or later any control plane will break.

## Slide 10: Scenario: Egress Link Overload
OvS
NIC
PMD 1
PMD 2
ovs-vswitchd thread
Tenant VM
BFD
LACP
RSS
VIM Components
Host networking
br-ctl
PMD Tx queues full. Tenant data being dropped.
Separate Tx queue for ovs-vswitchd. HW scheduler can provide fair share of link band-width
Egress link band-width exhausted by tenant data
Notes: The other overload scenario is link overload before PMD overload. This is more likely to happen with large packets.
Congestion of the links into a compute can be handled through QoS configuration on the ToR switches. But what about link congestion in the egress direction caused by the VM sending a lot of data in large packets?
As you can see, in this case the Tx queues of the NIC dedicated to PMDs run full so that the PMDs will drop excess tenant data packets.
However, as the vswitchd thread has its own Tx queue the control plane packets are not directly affected. If the NIC performs some fair scheduling of Tx queues, there should be sufficient bandwidth available for the control plane Tx queue to not cause packet drop.
We will not have a look at measurements done in a test NFVI deployment to verify the effects of tenant data overload on control plane.

## Slide 11: Measurements Impact of PMD Overload
Packet drops in the Rx queue of physical port equally affect tenant data, BFD and OVS control plane packets
“ping –f“ to br-ctl interface to quantify control plane impact
  Ping packet drop in line with overall packet drop
  RTT jumps from 50 us to 3 ms
BFD flapping occurs already at moderate overload
  The rate increases with overload
Above 45% packet drop the OpenFlow control channel breaks due to missed Echo Replies
source: Ericsson
CPU: Dual socket, Xeon CPU E5-2697 v3 @ 2.60GHz, 14 cores + HT, 896K L1, 3584K L2, 35MB L3 cache; NIC: Intel Fortville X710, 4 x 10Gbit/s; OvS: version 2.6, 1 PMD, 1 phy port, 1 vhostuser port; VM: TRex DPDK traffic source/sink
Notes: To check the effect of PMD overload we sent 64 byte packets with a traffic generator through a VXLAN tunnel into a physical port polled by a single PMD.
Decapsulated packets were forwarded by OVS into the tenant VM with the standard OpenStack Neutron setup with OpenDaylight as SDN controller.
The VXLAN tunnel was supervised with BFD. (No bond and LACP in this test.)
In parallel we ran “ping -f” to the br-ctl interface on the compute over the same link to simulate and measure control plane impact.
At a load of 2200 Kpps, the PMD load was at 100% with practically zero packet drop. This constituted the maximum forwarding rate.
From there we increased the traffic generator load in steps up to 4000 Kpps (82% overload) and checked the effect on the system.
The fraction of dropped Ping packets at each overload level exactly matches the expected packet drop.
The ping RTT jumps from 50 us to 3 ms immediately. This jump is due to buffering time the passed packets now spend in the full NIC Rx queue (2K entries).
Even with moderate overload (10% drop) we see the first BFD flap events. Their frequency increases with the amount of overload. PMD flapping raises alarms and can even trigger failover/re-routing actions by OVS or even the SDN controller.
Above 45% packet drop the OpenFlow control channel breaks due to too many missed Echo Reply packets. This can cause serious service interruption.
All in all we must take note that such a system is not well protected against uncontrolled tenant data overload.

## Slide 12: Measurements Impact of Egress Link Overload
Egress link overload does not affect the control plane
  Outgoing packets are forwarded by the ovs-vswitchd thread, which has its dedicated TX queue in the Fortville NIC
  The NIC schedules packets from each of the TX queues in some fair manner, so that the ovs-vswitchd queue gets sufficient bandwidth on the link
Incoming packets are not affected as neither link nor PMDs are overloaded
  No BFD flapping
source: Ericsson
CPU: Dual socket, Xeon CPU E5-2697 v3 @ 2.60GHz, 14 cores + HT, 896K L1, 3584K L2, 35MB L3 cache; NIC: Intel Fortville X710, 4 x 10Gbit/s; OvS: version 2.6, 1 PMD, 1 phy port, 1 vhostuser port; VM: TRex DPDK traffic source/sink
Notes: Our second measurement proves that the dedicated Tx queue OVS uses on the Intel Fortville NIC for the ovs-vswitchd thread effectively protects the control plane against egress link overload.
There is no Ping packet drop and the RTT only increases from 100 to 200 us, which should not have any visible effect on real control plane.
We have reason to believe that other NICs with sufficiently many Tx queues and a reasonable Tx scheduling algorithm will exhibit very similar behavior.
In summary, our measurements show that the effect of PMD overload on ingress control plane packets is the main OVS-DPDK risk.

## Slide 13: Use Case 3: QoS for Tenant Data
All tenant data traffic is equal!?
Well, some packets are more equal than others!
Virtual Network Functions send/receive a large variety of network traffic
  Top prio: Critical internal control plane (e.g. cluster membership)
  …
  Min prio: Bulk user plane
VNFs need prioritization for their critical traffic in the NFVI
How to orchestrate and implement the necessary QoS end-to-end?
Will need additional priority levels and packet marking (e.g. IP Diffserv)
Notes: So far we have pretended that all tenant data traffic is equal.
That was, of course, a myth. ”Some packets are more equal than others!”
In reality NFV infrastructure including OVS will have to be able to provide end-to-end (VM-to-VM) QoS for different classes of tenant traffic to be able to execute host VNFs.
Just consider the difference between e.g. a cluster membership protocol between VMs in a VNF and the bulk tenant user plane.
There are many open questions when it comes to the orchestration of e2e QoS for tenant data, but it is obvious that we will have to consider several priority levels for tenant data below the priority reserved for infrastructure control plane.
And it is likely that NFVIs will make use of established QoS schemes like Diffserv to represent QoS classes of packets on the network fabric.

## Slide 14: Desired Ingress Prioritization on Physical Ports
Priority 1: In-band control plane
  Untagged LACP packets
  BFD packets inside tunnel based on IP DSCP of outer IP header
Priority 2: VIM control plane
  Certain prioritized VLAN tags
Priority 3+: Prioritized tenant data
  E.g. based on IP DSCP of outer IP header
Base Priority
  Non-prioritized traffic spread through RSS over multiple Rx queues
Notes: Here’s a summary of the different priority classes and possible classification filters we would want for the NFVI deployments we are looking at today.
Let me now hand over to Billy to explain what he has been doing to address the need for ingress scheduling in OvS-DPDK.

## Slide 15: Ingress Scheduling
PMD
“Schedulers arrange and/or rearrange packets for output.”
-- http://www.tldp.org/HOWTO/html_single/Traffic-Control-HOWTO/#e-scheduling
RX Queue

TX Queue

?
ovs-vswitchd
BFD
LACP
Priority packet – e.g control plane.
Notes: When we started this work it was in the context of reducing packet latencies for telecoms/real-time applications.
The idea was that if a high priority packet like these orange guys here could ‘jump the queue’ so to speak then they would incur less latency.
We initially thought of an early stage classification mechanism in the userspace datapath to classify between priority and non-priority traffic. And then process one ahead of the other.
There are two problems with that:
* this classification effort would require a large effort relative to the overall packet processing budget.
* And what do you do with the lower priority traffic while you are dealing with the higher priority traffic? It has to go some where. This temporary storage of packets runs totally against the DPDK run-to-completion model. Which is designed to maximize cache effectiveness by avoiding temporary storage of packets.

## Slide 16: Ingress Scheduling - Implementation
RX Queue x2

TX Queue

?
DPDK rte_flow API installs rxq assignment filters on supported vendors NICs
ovs-vswitchd
BFD
LACP
PMD empties priority queue before reading non-priority queue
PMD
Notes: So we decided to leverage the multi-queue and queue assignment features of NICs.
Using DPDK rte_flow API, which will support several vendors NICs, we move the packet prioritization decision to the NIC.
As an aside we know that this is an area that is also WIP for Flow Classification Offload RFC and we would like to dovetail with that effort.
The NIC assigns prioritized packets to a extra priority queue.
The OvS reads “preferentially” from this priority RxQ.

## Slide 17: Ingress Scheduling - Implementation
Move packet prioritization decision to the NIC
Place prioritized packets on separate RX Queue
Read preferentially from “priority” RxQ. Keep it simple:
  Read from priority queue until it’s empty
  Service other queues
  Repeat
Notes: The preferential algorithm is really simple:
  Read from priority queue until it’s empty
  Service other queues
  Repeat
So as I said the original purpose of the ingress scheduling was to reduce latency for the prioritized packets.
So how did that work out?

## Slide 18: Ingress Scheduling – Latency effect
~99.9 % of packets already have have a latency <20us
There are x10 to x50 less packets in any given latency bucket – good.
But worst case latency does not improve.
CPU: Dual socket, Xeon(R) CPU E5-2695 v3 @ 2.30GHz 14 core no-HT, 896K L1, 3584K L2, 35MB L3 cache; NIC: Intel Fortville X710, 4 x 10Gbit/s; OvS: version 2.7.90, 1 PMD, 2 phy port, Hardware traffic source/sink
Source: Intel
Notes: Well, okay.
Notice there is a log scale on this graph.
– provided traffic that did not need to go to a VM
and worst case latency was not reduced

## Slide 19: Ingress Scheduling – Overload protection
RX Queue x2

TX Queue


?
ovs-vswitchd
BFD
LACP
PMD 1
Notes: But the other thing we realised was by using an additional rx queue for priority traffic was that in an overloaded situation the finite length of the RX queues served as a natural load shedder for lower priority traffic while still allowing higher priority traffic to be processed.
Because there are relatively more rx queue descriptors for priority that non-priority packets. The non-priority packets are shedded ahead of the priority packets. And they are shedded without any PMD cycles being expended.
And we’ve seen this in results of some experiements Jan has performed..

## Slide 20: Ingress Scheduling – Traffic Protection
dpdk1
Overload PMD through 64 byte DPDK traffic on dpdk0
   100% PMD load in pmd-stats-show
   25% rx packet drop on dpdk0
Add iperf3 UDP traffic (256 bytes) in parallel over dpdk1
Measurement result:
SUT Server
OvS
VM dpdk testpmd
vhostuser
iperf3 udp server
PMD
br-prv
ToR
dpdk0
dpdk1
TGen Server
BM dpdk pktgen
iperf3 udp client
dpdk0
Low priority
High/Low priority
source: Ericsson | Condition 1 dpdk1 low priority | Condition 2 dpdk1 high priority
iperf3 UDP throughput | not measured | 1 Gbit/s 460 Kpps 1)
iperf3 UDP packet loss | 28% | 0%
1) iperf3 throughput limited by UDP/IP stack on client side
CPU: Dual socket, Xeon CPU E5-2680 v4 @ 2.40GHz, 14 cores + HT, 896K L1, 3584K L2, 35MB L3 cache NIC: Intel Fortville X710, 4 x 10Gbit/s; OvS: version 2.6, 1 PMD, all ports and VM on NUMA node 0
Notes: Okay - here comes the science bit.
This experiment is based on using the simple prioritized reading mechanism I outlined earlier.
Full-disclosure: There is a small difference in that instead of one NIC classifying traffic on to two low and high priority queues there are two NICS each with one queue. But that is doesn’t matter as the pmd main thread deals with reading from individual queues. It doesn’t know or care if they are the same NIC or not.
First we saturate the the pmd with low-priority traffic via the green line from the Traffic gen to the SUT. So we bring the PMD up to 100% of cycles spent processing packets.
Then we run two iterations of the experiment. With two different conditions.
Condition One: The rxq for the orange line entering the SUT server is treated as normal
Condition Two: The rxq for the orange line entering the SUT server is read from preferentially – with the simple method outlined previously
With no prioritization for the tan line iperf3 reports 28% of UDP packets are lost which is as you’d expect it suffers about the same loss rate as OvS reports for the green line.
When prioritization is enabled for the orange line we see that there is zero packet loss. Even though it is receiving traffic as fast as iperf can pump it out from the traffic generator – 1 Gbit/s.

## Slide 21: Ingress Scheduling – Configuration
$ ovs-vsctl set Interface phy1
ingress_sched:
eth_type=0x8809
Field as per ovs-fields(7) and ofctl add-flow. Not all netdevs/NICs will support all combinations.
Single prioritization condition.
Notes: I won’t delay through the next several slides.
Mainly I want to show that the syntax for the match filters is compatible with the ofctl syntax as outlined in ovs-fields man page. Obviously no netdev would be expected to support anywhere near all the fields but that syntax is already familiar to OvS users so it’s the principle of least-surprise.
This slide shows a super simple prioritization configuration – which is all that is supported in the current RFC patch.

## Slide 22: Ingress Scheduling – Configuration (future)
$ ovs-vsctl set Interface phy1
ingress_sched:
vlan_tci=0x1123/0x1fff,ip,ip_dscp=0x5
Several different prioritization conditions. a AND b.
Notes: Multiple conditions. AND’ed together as you’d expect.

## Slide 23: Ingress Scheduling – Configuration (future)
$ ovs-vsctl set Interface phy1
ingress_sched:
filter=vlan_tci=0x1123/0x1fff
filter=ip,ip_dscp=0x5
Several different prioritization conditions. a OR b.
Notes: Multiple conditions OR’d together.

## Slide 24: Ingress Scheduling – Configuration (future)
$ ovs-vsctl set Interface phy1
ingress_sched:
prio=1,
filter,vlan_tci=0x1123/0x1fff,
filter,eth_type=0x8809,
prio=2,
filter,ip,ip_dscp=0x5,
Traffic Priority Levels
Support several levels of prioritization: High and Low but also a Critical level for instance.
Notes: Different levels of prioritization. This is a little more future looking but we wanted to think ahead to ensure we didn’t have to undo any configuration we had only just specified.

## Slide 25: Ingress Scheduling – Configuration (future)
$ ovs-vsctl set Interface phy1
ingress_sched:
prio=2,
filter,ip,ip_dscp=0x5,
prio=1,
filter=vlan_tci=0x1123/0x1fff,
filter,eth_type=0x8809
Filter Priority:
Filter groups are applied in the order in which they appear on the configuration line.
Notes: Finally some applications may find it really useful to apply some filters in a particular order.
This is supported by the rte_flow API. But when dealing with real NICs and DPDK driver implementations then you mileage may vary.

## Slide 26: Ingress Scheduling –Error reporting
ovsdb-schema
<table name="Interface"…
<column name="ingress_sched" key="err">
      If the specified ingress scheduling could not be applied, Open vSwitch sets this column to an error description in human readable form. Otherwise, Open vSwitch clears this column.
Notes: On that note - error reporting. Similar to other error reporting mechanisms in OvS. The netdev can report a human readable string via ovsdb if the specified ingress scheduling configuration could not be applied.

## Slide 27: Ingress Scheduling – RxQ’s & RSS
$ ovs-vsctl set Interface phy1
options:n_rxq=4
$ ovs-vsctl set Interface phy1
ingress_sched:
prio=2,
filter,ip,ip_dscp=0x5,
prio=1,
filter=vlan_tci=0x1123/0x1fff,
filter,eth_type=0x8809
RSS queues
Additional Priority Queues
Notes: Also to note that prioritization queues are over and above the number of queues specified normally for the interface. So on this configuration here non-priority packets are RSS’d as normal across the 4 rxqs on the Interface table and packets matching the priority filters would have their own additional queues.

## Slide 28: Ingress Scheduling – Next Steps
PMD
PMD
PMD
PMD
Avoid poor rxq -> pmd assignment
Notes: Kevin Traynor has done some great work recently to rebalance rxqs amongst PMDs so that OvS doesn’t end up with a really poor load allocation over time. We intend to build on that work for the same ends so that priority queues also don’t all get allocated to the same PMD.

## Slide 29: Ingress Scheduling – Next Steps
Use rte_flow API for offload
Extend to several priorities
    Priorities of overlapping filters
    Multiple traffic priorities
Working with RFC ‘Flow Offload’ feature…
…
Prioritization to the Guest…

## Slide 30: Summary
OvS-DPDK in NFVI context needs ingress scheduling to protect priority traffic against PMD overload
SW priority queue handling in the PMD loop is effective
  Could be upstreamed first, priority configurable per port
Off-loading classification and queue selection to NIC through rte_flow API allows generic solution
  Interaction with RFC Flow Classification Offload
Work in progress
  Lots left to figure out
  We are open for suggestions/collaboration
Notes: So let’s recap what we have shown:
OVS DPDK has great performance but is lacking ingress scheduling to needed to provide necessary protection of priority traffic.
The PMD main loop can easily be enhanced to effectively support Rx queues with multiple strict priority levels.
Such a change could be upstreamed separately to support priority configurable per port.
The classification for queue selection should be offloaded to the NIC through the rte_flow API for a generic solution.
However, the Flow Classification Offload work is working with the same API. We’ll need coordination here.
There is a lot of work left and we are more than happy to receive suggestions and open for collaboration.

## Slide 31: Intel Notices & Disclaimers
Intel technologies’ features and benefits depend on system configuration and may require enabled hardware, software or service activation. Performance varies depending on system configuration. Check with your system manufacturer or retailer or learn more at intel.com.
No computer system can be absolutely secure.
Tests document performance of components on a particular test, in specific systems. Differences in hardware, software, or configuration will affect actual performance. Consult other sources of information to evaluate performance as you consider your purchase. For more complete information about performance and benchmark results, visit http://www.intel.com/benchmarks .
Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark and MobileMark, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products. For more complete information visit http://www.intel.com/benchmarks .
Intel's compilers may or may not optimize to the same degree for non-Intel microprocessors for optimizations that are not unique to Intel microprocessors. These optimizations include SSE2, SSE3, and SSSE3 instruction sets and other optimizations. Intel does not guarantee the availability, functionality, or effectiveness of any optimization on microprocessors not manufactured by Intel. Microprocessor-dependent optimizations in this product are intended for use with Intel microprocessors. Certain optimizations not specific to Intel microarchitecture are reserved for Intel microprocessors. Please refer to the applicable product User and Reference Guides for more information regarding the specific instruction sets covered by this notice.
Cost reduction scenarios described are intended as examples of how a given Intel-based product, in the specified circumstances and configurations, may affect future costs and provide cost savings. Circumstances will vary. Intel does not guarantee any costs or cost reduction.
Intel does not control or audit third-party benchmark data or the web sites referenced in this document. You should visit the referenced web site and confirm whether referenced data are accurate.
© 2017 Intel Corporation.
Intel, the Intel logo, and Intel Xeon are trademarks of Intel Corporation in the U.S. and/or other countries.
*Other names and brands may be claimed as property of others.

## Slide 32: Thank You! Questions?

## Slide 33: References
[ovs-dev] [RFC PATCH 0/3] prioritizing latency sensitive traffic
  [ovs-dev,RFC,1/3] netdev: Add set_ingress_sched to netdev api
  [ovs-dev,RFC,2/3] netdev-dpdk: Apply ingress_sched config to dpdk phy ports
  [ovs-dev,RFC,3/3] dpif-netdev: Add rxq prioritization